## Slide 1
EC10 OUTPUT
Lift Control Management
Floor Button
Panel
When EC10 work well
NC and COM is disconnect, so there is no response event user press the button
Only when user punch on Reader of device, and successfully, the NC and COM is shorted.
floor1
floor2
floor1
floor2
FR1200
1. Punch on reader
2. Verify successfully
This user have access to go floor1
3. Right now, floor 1 button is available.
4. If user press button, lift control get the signal and move to floor1

## Slide 2
If EC10 is power off, or fire alarm(IN9 is shorted), the NC and COM is connected
It work like following diagram, EC10 didn’t control the elevator
EC10 OUTPUT
Lift Control Management
Floor Button
Panel
User press button, then lift control management get the signal.